Autonetwork example

All references in this document refer to document DPA Framework Technical Guide v.3.00

Used firmware on TR modules:

1 x GeneralHWP-Coordinator-STD-SPI-7xD-V300-170314.iqrf with the
      CustomDpaHandler-Coordinator-AutoNetwork-7xD-V300-170314.hex
6 x GeneralHWP-Node-STD-SPI-7xD-V300-170314.iqrf with the
      CustomDpaHandler-AutoNetwork-7xD-V300-170314.hex

(Do not forget to enable custom handler in TR configuration for HWP)
Before compilation of Autonetwork example source code, the __STORE_CODE_SUPPORT__ configuration switch of DPA support library in dpa_library.h file should by disabled.

List of commands:

- rst	- print header of Console command processor

- ledr on „NADR“	- see chapter 3.9.2 Set
- ledr off „NADR“	- see chapter 3.9.2 Set
- ledr pulse „NADR“	- see chapter 3.9.4 Pulse

- clrbonds - clears all bonded nodes in coordinator, unbond all bonded nodes and execute their restart. ( see chapter 3.2.5 Clear all bonds, chapter 3.3.3 Remove bond, chapter 3.4.3 Reset ).

cmd> clrbonds

Remove all bonds at nodes and coordinator, restart nodes

- autontw 60 1 1 25 1	- command to start Autonetwork algorithm where:

60 = temporary address timeout
1 = authorize retries
1 = discovery retries
25 = prebonding interval
1 = TX power

It is possible to use autontw command without parameters. In this case Autonetwork algorithm use its default parameters.
60 = temporary address timeout
1 = authorize retries
1 = discovery retries
35 = prebonding interval
1 = TX power

Algorithm round 1.

cmd> autontw 60 1 1 25 1

Automatic network construction started
Getting initial network info

Round=1, Nodes=0, New nodes=0
Enable prebonding at coordinator, mask=0, time=60
Waiting for prebonding for 25 seconds
Disable prebonding at coordinator
Coordinator prebonded MID=8100881E, UserData=02046E39
Coordinator prebonded MID=81102D5A, UserData=02046E39
Coordinator prebonded MID=81008831, UserData=02046E39
Coordinator prebonded MID=81102D56, UserData=02046E39
Coordinator prebonded MID=81102D60, UserData=02046E39
Coordinator prebonded MID=81004A57, UserData=02046E39
Authorizing node MID=8100881E, address 1
OK, nodes count=1
Authorizing node MID=81102D5A, address 2
OK, nodes count=2
Authorizing node MID=81008831, address 3
OK, nodes count=3
Authorizing node MID=81102D56, address 4
OK, nodes count=4
Authorizing node MID=81102D60, address 5
OK, nodes count=5
Authorizing node MID=81004A57, address 6
OK, nodes count=6
Running FRC to check new nodes and removing 0xFE nodes
Remote unbonding node 2
Removing node 2
Running discovery
Discovered nodes=5
Waiting for coordinator to finish discovery

Algorithm round 2.

Algorithm round 3.

Round=2, Nodes=5, New nodes=5
Enable prebonding at nodes, mask=7, time=60, LEDR=1
Enable prebonding at coordinator, mask=7, time=60
Waiting for prebonding for 25 seconds
Disable prebonding at coordinator
Running FRC to disable and check for prebonding
Node 3 prebonded MID=81102D5A, UserData=3D046E74
Authorizing node MID=81102D5A, address 7
OK, nodes count=6
Running FRC to check new nodes and removing 0xFE nodes
Running discovery
Discovered nodes=6
Waiting for coordinator to finish discovery

Round=3, Nodes=6, New nodes=6
Enable prebonding at nodes, mask=7, time=60, LEDR=1
Enable prebonding at coordinator, mask=7, time=60
Waiting for prebonding for 25 seconds
Disable prebonding at coordinator
Running FRC to disable and check for prebonding
No new node prebonded

Autonetwork algorithm is possible to end anytime, when you type Q or q and hit ENTER.

Round=4, Nodes=6, New nodes=6
Enable prebonding at nodes, mask=7, time=60, LEDR=1
Enable prebonding at coordinator, mask=7, time=60
Waiting for prebonding for 25 seconds
Disable prebonding at nodes
Disable prebonding at coordinator
Automatic network construction stopped

cmd>